## Slide 1: Small Reflector Splash Plate BOR-MOM Design
Tom Milligan
www.antennadesigner.org
Small Reflector BOR-MoM Design

## Slide 2
Section 8-23 Small Reflector Splash Plate BOR-MoM Design Modern Antenna Design 2ed. addition download (website)
7-3.5 External Wall Horn Corrugations Modern Antenna Design 2ed. addition download (website)
Start with Turrin Horn Feed (0.62λ diameter) CHAMP model
Add variable external Corrugations to Turrin Horn
Use Displaced axis reflector with spline defined reflectors
Extended exterior of Turrin Horn to Main Reflector Hole
Use CHAMP optimization to Design Reflector
Small Reflector BOR-MoM Design

## Slide 3
Initial Turrin Horn Feed for Small Reflector

## Slide 4
Use input file to COWSDT (Section 7-3.5) for Ext. Corrugations
1 single corrugations
cowsdt6235t.txt
19.567 aperture outer radius
3 mm
0 z-position radius at aperture
19.567 radius of final corrugation
182.7 z postion end of corrugations
35 number of corrugations
.75 corrugation thickness
5 distance to first corrugation
3 # variable corrugations
7.5 1st corrugation height
5 distance between two corrugations
7.5 2nd corrugation height
5 distance between two corrugations
7.5 3rd corrugation height
7.5,7.5 remaining corrugation heights

## Slide 5
Replace “horn_exterior” with output from COWSDT

## Slide 6
External Corrugations added to Turrin Feed

## Slide 7
Use DAXSG to Design and Generate CHAMP Spline Reflectors
Displaced axis Gregorian single offset dimensions
Main reflector focal length 200.2500
Subreflector diameter: 82.5000
Main diameter: 750.0000
Feed half subtended angle: 52.00
Effective f/D: 0.51258
Focus Axis length: 17.538
Main Vertex to feed: 182.712
Feed to subreflect.: 25.100
Main diameter: 750.000
Main reflector depth: 139.062
Subreflector dia: 82.500
Vertex to subr. Top: 217.903
Axis tilt: 66.97
Feed subtended angle: 104.00
Ellipse 2*C: 44.823
Eccentricity: 0.66863

## Slide 8
CHAMP spline main reflector
ring_focus_main_reflector spline_circ_sym_reflector
(
z_offset : "ref(z_focal_point)" mm,
length_unit : mm,
nodes : table
(
2.710000E+01 "ref(zmain1)"
6.189000E+01 "ref(zmain2)"
9.668000E+01 "ref(zmain3)"
1.314700E+02 "ref(zmain4)"
1.662600E+02 "ref(zmain5)"
2.010500E+02 "ref(zmain6)"
2.358400E+02 "ref(zmain7)"
2.706300E+02 "ref(zmain8)"
3.054200E+02 "ref(zmain9)"
3.402100E+02 "ref(zmain10)"
3.750000E+02 "ref(zmain11)"
)
)

## Slide 9
CHAMP spline Subreflector
ring_focus_sub_reflector spline_circ_sym_reflector
(
z_offset : "ref(z_focal_point)" mm,
length_unit : mm,
nodes : table
(
0.000000E+00 "ref(zsub1)"
4.583333E+00 "ref(zsub2)"
9.166667E+00 "ref(zsub3)"
1.375000E+01 "ref(zsub4)"
1.833333E+01 "ref(zsub5)"
2.291667E+01 "ref(zsub6)"
2.750000E+01 "ref(zsub7)"
3.208334E+01 "ref(zsub8)"
3.666667E+01 "ref(zsub9)"
4.125000E+01 "ref(zsub10)"
)
)
These two reflectors are added to the scatterers list at the top of the geometry.tor file.
scatterers : sequence(ref(horn_exterior),ref(ring_focus_sub_reflector),ref(ring_focus_main_reflector))
)

## Slide 10
External Corrugated Feed w/ Main & Subreflector

## Slide 11
Displaced Axis Dual Reflector w/ External Corrugated Feed

## Slide 12
Optimization Goals:
  Max. Bore Sight Directivity
  Max. Return Loss
  Sidelobe Template:
    29 – 25 Log ϴ for 1.5˚ ≤ ϴ ≤ 7˚
    8 dBi for 7˚ ≤ ϴ ≤ 9.2˚
    32 – 25 Log ϴ for 9.2˚ ≤ ϴ ≤ 48.2˚
    -10 dBi for 48˚ ≤ ϴ ≤ 180˚
Optimization Variables
  Main and Subreflector z-values of Splines
  1st 3 External Corrugations and Their Spacing
Small Reflector BOR-MoM Design CHAMP Optimization

## Slide 13
Small Reflector BOR-MoM Design Initial Optimization

## Slide 14
Add Dielectric Subreflector Support Cone, Re-Optimize

## Slide 15
Input File to CHSCONE.EXE Dielectric Support Cone
chscone1t.txt
3 units: mm
support_cone
2.9,1.0,.004 dielectric constant, permability, loss tangent
2.5 thickness
18.567 inner radius of horn
82.5,10 subreflector diameter, # in spline
1.5 subreflector support extension
1.5 support depth at subreflector
1.5 support along horn
Generates addition to CHAMP geometry.tor file

## Slide 16
Elements of geometry bor_mesh for Dielectric Support Cone
support_cone bor_mesh
(
regions : table
(
1 2.9000E+00 1.0000E+00 4.0000E-03
),
nodes : table
(
1 "ref(ZSC1)" "ref(RSC1)"
2 "ref(ZSC2)" "ref(RSC2)"
3 "ref(ZSC3)" "ref(RSC3)"
4 "ref(ZSC4)" "ref(RSC4)"
5 "ref(ZSC5)" "ref(RSC5)"
6 "ref(ZSC6)" "ref(RSC6)"
7 "ref(ZSC7)" "ref(RSC7)"
8 "ref(ZSC8)" "ref(RSC8)"
),
linear_segments : table
(
1 1 2 0 1 -1.0 0.0
1 2 3 0 1 0.0 0.0
1 3 4 0 1 -1.0 0.0
1 4 5 0 1 -1.0 0.0
1 5 6 0 1 -1.0 0.0
1 6 7 0 1 0.0 0.0
1 7 8 0 1 0.0 0.0
),
length_unit : mm
)
ZSC2 real_variable
(
value : "ref(ZSUB10)+ref(Z_FOCAL_POINT)"
)
ALSC real_variable
(
value : "SQRT((ref(ZSC2)-ref(ZSC1))**2+(ref(RSC2)-ref(RSC1))**2)"
)
UZSC real_variable
(
value : "(ref(ZSC2)-ref(ZSC1))/ref(ALSC)"
)
URSC real_variable
(
value : "(ref(RSC2)-ref(RSC1))/ref(ALSC)"
)
ZSC4 real_variable
(
value : "ref(ZSC2)+ref(DEPTH)"
)
RSC5 real_variable
(
value : "ref(RSC2)+(ref(TSC1)+ref(URSC)*ref(DEPTH))/ref(UZSC)"
)
RSC6 real_variable
(
value : "def(RW1)+(ref(TSC1)-ref(URSC)*ref(HSL))/ref(UZSC)"
)

## Slide 17
Modifications to geometry.tor file for Dielectric Cone
horn combined_horn_section
(
horn_sections : sequence(ref(circular_waveguide_section),ref(smooth_horn_section),
ref(smooth_horn_section_0001)),
scatterers : sequence(ref(horn_exterior),ref(ring_focus_sub_reflector),ref(ring_focus_main_reflector),
ref(support_cone))
)
horn_exterior circular_symmetric_horn_exterior
(
snap_to_aperture : off,
length_unit : mm,
nodes : table
(
"-ref(ZW1)" "ref(RW1)"
"-ref(ZC1)" "ref(RC1)"
"-ref(ZC1)" "ref(RC1)+ref(C1)"
"-ref(ZC1)-ref(CT)" "ref(RC1)+ref(C1)"
"-ref(ZC1)-ref(CT)" "ref(RC1)"
"-ref(ZC2)" "ref(RC2)"
"-ref(ZC2)" "ref(RC2)+ref(C2)"
"-ref(ZC2)-ref(CT)" "ref(RC2)+ref(C2)"
RW1 real_variable
(
value : 19.567
)
ZW1 real_variable
(
value : 1.5
)
struct(variable_object: ref(D1), min: 2.0, max: 7.0),

## Slide 18
Pattern of Optimized Antenna including Support Cone

## Slide 19
Small Reflector with Sinusoidal Feed Tube Corrugations

## Slide 20
Small Reflector BOR-MoM Sinusoidal Corrugation Input
COWSPLI.EXE Generates Horizontal Sinusoidal
Spline for geometry.tor (Section 7-3.5)
Input File:
cowspli1t.txt
19.567 aperture outer radius
3 mm
0. initial Z-position
19.567 aperture outer radius
182.7 z postion end of corrugations
3,25 # sinusoids, #spline points
7.5 spline total height
35. distance to spline
38. length of spline

## Slide 21
Sinusoidal outer Corrugation 25 Points
sinusoid_outer circular_symmetric_horn_exterior
(
snap_to_aperture : off,
length_unit : mm,
nodes : table
(
"-ref(ZC1)-0.00000e+00" "ref(RD)*(ref(ZC1)+0.00000e+00)/ref(ZD)+ref(RW2)+ref(RSP1)"
"-ref(ZC1)-1.58333e+00" "ref(RD)*(ref(ZC1)+1.58333e+00)/ref(ZD)+ref(RW2)+ref(RSP2)"
"-ref(ZC1)-3.16667e+00" "ref(RD)*(ref(ZC1)+3.16667e+00)/ref(ZD)+ref(RW2)+ref(RSP3)"
"-ref(ZC1)-4.75000e+00" "ref(RD)*(ref(ZC1)+4.75000e+00)/ref(ZD)+ref(RW2)+ref(RSP4)"
"-ref(ZC1)-6.33333e+00" "ref(RD)*(ref(ZC1)+6.33333e+00)/ref(ZD)+ref(RW2)+ref(RSP5)"
"-ref(ZC1)-7.91667e+00" "ref(RD)*(ref(ZC1)+7.91667e+00)/ref(ZD)+ref(RW2)+ref(RSP6)"
"-ref(ZC1)-9.50000e+00" "ref(RD)*(ref(ZC1)+9.50000e+00)/ref(ZD)+ref(RW2)+ref(RSP7)"
"-ref(ZC1)-1.10833e+01" "ref(RD)*(ref(ZC1)+1.10833e+01)/ref(ZD)+ref(RW2)+ref(RSP8)"
"-ref(ZC1)-1.26667e+01" "ref(RD)*(ref(ZC1)+1.26667e+01)/ref(ZD)+ref(RW2)+ref(RSP9)"
"-ref(ZC1)-1.42500e+01" "ref(RD)*(ref(ZC1)+1.42500e+01)/ref(ZD)+ref(RW2)+ref(RSP10)"
"-ref(ZC1)-1.58333e+01" "ref(RD)*(ref(ZC1)+1.58333e+01)/ref(ZD)+ref(RW2)+ref(RSP11)"
"-ref(ZC1)-1.74167e+01" "ref(RD)*(ref(ZC1)+1.74167e+01)/ref(ZD)+ref(RW2)+ref(RSP12)"
"-ref(ZC1)-1.90000e+01" "ref(RD)*(ref(ZC1)+1.90000e+01)/ref(ZD)+ref(RW2)+ref(RSP13)"
"-ref(ZC1)-2.05833e+01" "ref(RD)*(ref(ZC1)+2.05833e+01)/ref(ZD)+ref(RW2)+ref(RSP14)"
"-ref(ZC1)-2.21667e+01" "ref(RD)*(ref(ZC1)+2.21667e+01)/ref(ZD)+ref(RW2)+ref(RSP15)"
"-ref(ZC1)-2.37500e+01" "ref(RD)*(ref(ZC1)+2.37500e+01)/ref(ZD)+ref(RW2)+ref(RSP16)"
"-ref(ZC1)-2.53333e+01" "ref(RD)*(ref(ZC1)+2.53333e+01)/ref(ZD)+ref(RW2)+ref(RSP17)"
"-ref(ZC1)-2.69167e+01" "ref(RD)*(ref(ZC1)+2.69167e+01)/ref(ZD)+ref(RW2)+ref(RSP18)"
"-ref(ZC1)-2.85000e+01" "ref(RD)*(ref(ZC1)+2.85000e+01)/ref(ZD)+ref(RW2)+ref(RSP19)"
"-ref(ZC1)-3.00833e+01" "ref(RD)*(ref(ZC1)+3.00833e+01)/ref(ZD)+ref(RW2)+ref(RSP20)"
"-ref(ZC1)-3.16667e+01" "ref(RD)*(ref(ZC1)+3.16667e+01)/ref(ZD)+ref(RW2)+ref(RSP21)"
"-ref(ZC1)-3.32500e+01" "ref(RD)*(ref(ZC1)+3.32500e+01)/ref(ZD)+ref(RW2)+ref(RSP22)"
"-ref(ZC1)-3.48333e+01" "ref(RD)*(ref(ZC1)+3.48333e+01)/ref(ZD)+ref(RW2)+ref(RSP23)"
"-ref(ZC1)-3.64167e+01" "ref(RD)*(ref(ZC1)+3.64167e+01)/ref(ZD)+ref(RW2)+ref(RSP24)"
"-ref(ZC1)-3.80000e+01" "ref(RD)*(ref(ZC1)+3.80000e+01)/ref(ZD)+ref(RW2)+ref(RSP25)"

## Slide 22
Small Reflector BOR-MoM Optimized Sinusoidal Corrugations
scatterers : sequence(ref(horn_exterior),ref(ring_focus_sub_reflector),
ref(ring_focus_main_reflector),ref(support_cone),ref(horn_exterior_2),
ref(sinusoid_outer))
)

## Slide 23
Small Reflector BOR-MoM Optimized Sinusoidal Corrugations